## Slide 1
BESS

## Slide 2: BESS in India: demand, government target and present situation
Government wants 41.65 GW of BESS by FY30; about 9.6 GWh is operating today, against ~151 GWh already tendered
Government targets and support
Item | Detail
CEA target, FY2029-30 | 60.63 GW storage: 41.65 GW BESS + 18.98 GW pumped storage (PSP)
National Electricity Plan, FY2031-32 | ~73.9 GW (47.2 GW BESS + 26.7 GW PSP), ~411 GWh
Energy Storage Obligation (MoP) | 1% of consumption in 2023-24 rising to 4% by 2029-30; ≥85% of stored energy must be renewable
VGF tranche 1 (Mar 2024) | ₹3,760 cr for 13.2 GWh at ₹27 lakh/MWh
VGF tranche 2 (Jun 2025) | ₹5,400 cr from PSDF for 30 GWh at ₹18 lakh/MWh
ISTS charge waiver | 100% for co-located BESS commissioned by Jun 2028; falls 25% a year after that
Domestic content (Dec 2025) | ≥20% of BESS procurement cost must be local to get VGF; EMS software counts
CEA co-location advisory | New solar to add storage ≥10% of capacity, ≥2 hours (advisory, not mandatory)
Manufacturing | 10 GWh of ACC PLI earmarked for grid storage; Budget 2026-27 duty exemption on cell machinery
Demand outlook (storage requirement)
Source | Horizon | Requirement
CEA (Optimal Generation Mix) | FY2029-30 | 41.65 GW BESS
National Electricity Plan (CareEdge) | FY2031-32 | ~411 GWh (BESS + PSP)
IESA | 2035-36 | ~888 GWh total storage
Present situation (Oct 2026)
Metric | Figure
Installed BESS, Dec 2025 | 0.78 GWh
Installed BESS, H1 2026 | 8.7 GWh (8.2 GWh added in H1 2026)
Operational BESS, Aug 2026 | 9.6 GWh (mostly merchant projects)
Expected by end-2026 | >10 GWh
BESS tendered by Aug 2026 | 151 GWh (+ ~142 GWh PSP)
Source: [1] SolarQuarter (CEA roadmap, Feb 2026); [2] SolarQuarter (VGF, Aug 2026); [3] CareEdge via ANI; [5] Rubix via pv magazine India; [6] IESA via Angel One; [7] Mercom via ESS News; [8] IEEFA-JMK EnergyWatts Sep 2026; [10] JMK EnergyWatts Sep 2026; [14] Renewable Watch (ESO); [15] Energy-Storage.news (20% DCR)

## Slide 3: Why BESS is required: solar peaks at noon, demand peaks after sunset
India keeps adding solar and wind, but without storage the extra midday power is curtailed and the evening peak still needs coal
The problem
Issue | Evidence
Time mismatch | Solar output peaks around midday; peak demand comes in the evening after sunset
Capacity vs generation | Non-fossil ≈50% of installed capacity but only ≈29% of generation
Steeper duck curve | Morning ramp-down 28 GW (May 2025) → 50 GW (May 2026); evening ramp-up 68 → 80 GW
Solar wasted | ~8.1 TWh solar curtailed in Q1 FY27; Jul-Aug 2026: 1,462 MU solar + 373 MU wind curtailed while peak demand hit 270 GW
Why it is wasted | At midday supply exceeds demand and grid limits bite; with no storage the grid operator backs RE down
Storage today | ~9.6 GWh operational; meets only 1-2% of night-time peak
Why no other solution fills the gap
Option | Limitation
Coal plants | Ramp slowly and cannot go below ~55% minimum load; add emissions
Gas peakers | Little domestic gas; imported LNG is costly
Pumped hydro | Good for long duration but site-specific, 5-8 years to build; runs alongside BESS (18.98 GW target)
More transmission | Moves power between regions, but cannot move noon power to night
Demand response | Helpful but small scale today
BESS | Responds in under a second, built in ~18 months, sits at substations or solar parks
Solar and wind growth
As of | Solar | Wind | Solar + wind
Mar 2022 | 54.0 | 40.4 | 94.4
Mar 2023 | 66.8 | 42.6 | 109.4
Mar 2024 | 81.8 | 45.9 | 127.7
Mar 2025 | 105.6 | 50.0 | 155.6
Mar 2026 | 150.3 | 56 | 206
Sep 2026 | 171.1 | 59.2 | 230.3
FY2026: record 44.6 GW solar (+87% YoY) and 6 GW wind added.
H1 FY27: 20.8 GW solar and 3.1 GW wind added.
Solar has roughly tripled in 4.5 years; wind grew ~1.5×.
Mar 2026 wind is derived (Mar 2025 + 6 GW added).
Source: CareEdge via ANI (ramp, gen share); TaiyangNews/CREA (curtailment); IEEFA-JMK EnergyWatts Sep 2026; [Energetica India (Sep 2026 capacity); JMK via pv magazine India (FY2026); MNRE year-end physical progress; SolarQuarter (PSP target)

## Slide 4: BESS manufacturers: global leaders and Indian capacity
Global supply is concentrated in China; India has ~60 GWh of pack/container assembly but only ~2.5 GWh of operating cell capacity
Global top 5 BESS cell suppliers (2025)
Rank | Company | HQ
1 | CATL | China
2 | HiTHIUM | China
3 | EVE Energy | China
4 | BYD | China
5 | CALB | China
612 GWh of BESS cells shipped in 2025 (+95%); top 10 held ~89%, all Chinese.
India: top 5 BESS
Company | Location | Capacity | Status
Tata AutoComp–Gotion JV | Pune, Maharashtra | 6 GWh (full ramp) | Supplying Tata Power projects
Waaree ESS | Gujarat | 5.15 GWh (target 20 GWh) | Commissioned Jul 2026
JSW Energy | Pune, Maharashtra | 5 GWh | Commissioned Q4 FY26
Pace Digitek (Lineage Power) | Bidadi, Karnataka | 5 GWh (10 GWh by end-FY27) | 1.25 GWh built in first year
iNVERGY | Dasna, Uttar Pradesh | 3 GWh | Inaugurated (₹200 cr)
*Own calculation: nameplate capacity ÷ ~60 GWh national pack capacity (IEEFA). Also: Voltters 3 GWh (MP); planned Premier 6 GWh, VSL PowerHive 7.5 GWh, Powertrac 10 GWh, Neuron 5 GWh. Cells: Ola 2.5 GWh is the only operating cell plant, so most BESS cells are imported from China.
Source: Benchmark Mineral Intelligence; Wood Mackenzie via SolarQuarter; InfoLink via ESS News; Energetica India; Renewable Watch (Waaree); ESS News (Pace); pv magazine India (JSW); Energy-Storage.news (Tata AutoComp); IEEFA-JMK Jun 2026; IEEFA-JMK Sep 2026

## Slide 5
Basic structure of a BESS: from cell to grid
Main components
Component | What it does | India supply status
Battery cells (LFP) | Store the energy; about 60% of container price | Mostly imported from China; Indian lines just starting
BMS | Protects cells, balances them, estimates SOC/SOH | Mostly comes with imported battery systems
PCS / inverter | Converts DC↔AC; grid-forming and black start required for ≥50 MW from Apr 2027 | Global makers with Indian plants (Sungrow, Delta, Hitachi Energy)
Thermal management | Keeps cells in a narrow temperature band (liquid cooling) | Containers and HVAC local; chillers often imported
Fire and explosion safety | Gas/smoke detection, suppression in every container, venting | Available locally; mandatory under CEA rules from Apr 2027
Transformer & switchgear | Step up voltage, isolate faults, protection relays | Strong Indian manufacturing base
EMS / SCADA | Dispatch decisions, monitoring, reporting to SLDC | Indian developers; EMS counts toward 20% domestic content
Source: BESS Deep Research Report (ev repo, sections 3.3 and 4.3); IEEFA-JMK Sep 2026 (cell share of container price); Energetica India (CEA safety rules 2026); SolarQuarter (CEA technical standards 2026); Energy-Storage.news

## Slide 6
BESS technologies compared
LFP is about 90% of new lithium-ion storage; other chemistries fill niches (cold climate, very long duration, lithium-free supply)
Parameter | LFP | NMC | LTO | Sodium-ion | Vanadium flow (VRFB)
Nominal cell voltage | 3.2 V | 3.6-3.7 V | 2.3-2.4 V | ~2.8-3.2 V | ~1.26 V
Energy density (Wh/kg) | ~160-205 | ~200-280 | ~60-90 | ~100-175 (claims) | ~15-25 (electrolyte)
Cycle life | 6,000-10,000+ | 2,000-5,000 | 10,000-20,000+ | ~3,000-6,000 (claims) | >15,000
System round-trip efficiency (AC) | ~85-90% | ~85-90% | ~85-90% | ~80-88% | ~65-75%
Thermal safety | High | Medium-low | Very high | High | Non-flammable
Low-temperature charging | Poor below 0 °C | Moderate | Excellent | Good | Good
Critical materials | Lithium, graphite | Li, nickel, cobalt, graphite | Lithium, titanium | Sodium, hard carbon | Vanadium
Cost position (2026) | Lowest Li-ion | Higher | Highest Li-ion | Close to LFP, falling | High capex; cheap extra hours
Best fit | 2-4 h grid peak shifting | Space-constrained sites | Fast frequency response, cold sites | Lithium-free, cold climates | 8 h+ long duration, high cycling
Status for grid storage | Dominant | Legacy / niche | Niche | Early commercial (CATL mass production 2026) | Commercial niche (175 MW / 700 MWh in China)
Share of BESS production | ~90% of 2025 Li-ion storage additions | Part of remaining ~10% | Part of remaining ~10% | Small; not reported separately (60 GWh CATL storage order) | Small; not reported separately
Sources S&P Global Mobility: evolution of EV battery technology · Battery University BU-205 · InsideEVs: NMC, LFP and solid-state

## Slide 7
LFP cell components, materials and Indian suppliers
Cathode and anode are ~65% of cell cost and >90% are processed in China; India has started on cathode, anode, electrolyte and aluminium foil
Component | Material | Approx. per kWh* | Indian companies | Capacity / status
Cathode (CAM) | LiFePO₄ from lithium carbonate + iron phosphate | ~2 kg LFP; ~0.5-0.6 kg Li₂CO₃ | Himadri, GFCL EV, Altmin, Epsilon | Himadri 2,000 t by Dec 2026 → 40,000 t FY28; GFCL sales H2 FY27; lithium fully imported
Anode | Synthetic / natural graphite | ~1-1.2 kg | Epsilon, Himadri; HEG, PCBL entering | Epsilon 2,000 t (~2 GWh) → 30,000 t by 2028; Himadri 200 t (Apr 2026)
Electrolyte salt | LiPF₆ | ~0.6-0.8 kg electrolyte | GFCL, Neogen | GFCL commercial since Dec 2025; Neogen developing (Morita JV)
Solvents, additives | EC, DMC, EMC; VC, FEC | In electrolyte | Alkyl Amines, Balaji Amines, Acutaas | Supplying
Separator | PE/PP film, ceramic coated | Thin film | None at scale | Imported
Aluminium foil | Al, ~10-15 µm (cathode side) | ~0.25 kg | Hindalco | Sambalpur, commissioned Jan 2026; supports ~100 GWh
Copper foil | Cu, ~6-8 µm (anode side) | ~0.5 kg | None at scale | Imported
Binder | PVDF (cathode), CMC/SBR (anode) | Small | GFCL (PVDF) | Nearing qualification
Indian LFP cell makers relevant to BESS
Company | Location | Capacity | Status
Ola Cell Technologies | Krishnagiri, TN | 2.5 GWh operating | Only commercial cell producer; 46100 LFP cell BIS-certified
Exide Energy Solutions | Bengaluru, KA | 6 GWh Ph-I (3 GWh LFP prismatic) | Commissioned 23 Sep 2026; SVOLT licence
Reliance New Energy | Jamnagar, GJ | 40 GWh Ph-1 → 120 GWh | LFP / BESS focus; equipment delivered
Waaree Energies | Rambili, AP | 16 GWh integrated (₹8,175 cr) | Cells, packs and BESS; announced Feb 2026

## Slide 8
−
+
M
Electrons (e⁻)
Motor
Li⁺
Li⁺
Li⁺
Electrolyte
Anode (−)
graphite on copper foil
Separator
porous film, blocks e⁻
Cathode (+)
LFP on aluminium foil
Discharge: electrons travel round the wire and turn the motor; Li⁺ ions cross the electrolyte. Charging reverses both process.
Charger fills the tank
Stored water
= ENERGY (kWh)
Water height = VOLTAGE (V)
A taller column pushes harder
Tap = BMS
power limit
Motor
Height × flow= POWER (kW)
More height or dia of pipe ,more power
Flow = CURRENT (A)
Wh/kg = water held ÷ tank weight
LFP cells ≈ 175 · NMC cells ≈ 260 Wh/kg
Bigger tank = more range (kWh). Wider pipe = more power (kW). Same water in a lighter tank = higher Wh/kg. Time to empty = kWh ÷ kW.
Basics of Electrochemistry & Cell Working
Water Volume = Charge capacity (Ah)
Hydraulic Analogy for EV cell

## Slide 9
LFP Battery Manufacturing Process: Complete LiFePO4 Production Guide & Quality Control Standards
1. Making the LFP cathode powder
1 Raw materials
Iron phosphate (FePO₄) + lithium carbonate + a carbon source
2 Wet milling
Mixed in water and ground to sub-micron size in a bead mill
3 Spray drying
Slurry sprayed into hot air to form small round granules
4 Calcination
Kiln at ~700–800 °C in nitrogen: LiFePO₄ forms with a thin carbon coat
5 Finishing
Crush, sieve, remove magnetic iron, pack in dry bags
2. Making the cell: same core steps as every Li-ion cell
Electrode making
Mix LFP, carbon and binder into slurry
Coat on aluminium foil, then dry
Press (calender) and slit to width
Fine LFP powder is hard to disperse evenly; mixing quality drives cell-to-cell consistency.
Mostly large prismatic cells (e.g. BYD Blade); moisture must still be kept out.
LFP’s flat voltage curve makes faulty cells harder to spot; screening must be precise
Cell assembly (dry room)
Stack or wind with separator and graphite anode
Weld tabs, seal in can
Fill with electrolyte
Formation and testing
First slow charges build the SEI layer
Age for days, check self-discharge
Grade by capacity and resistance
LFP Manufacturing Process Overview

## Slide 10
Smaller BESS units: who sells them, including auto OEMs
Company | Type | Product and size | Price | How it is sold
Ola Electric | Indian 2W EV OEM | Ola Shakti home BESS: 1.5 / 3 / 5.2 / 9.1 kWh (Oct 2025) | ₹29,999 - ₹1,59,999 (intro, first 10,000) | Own 4680 'Bharat' cells; 4,000+ Ola stores; ₹999 reservation; deliveries from Jan 2026
Ola Electric | Indian 2W EV OEM | Shakti Gen2 4.6 / 9.2 kWh; C&I racks 38-257 kWh; Mahashakti 6.26 MWh (Aug 2026) | ₹99,999 / ₹1,74,999 (home) | LFP cell-to-pack in-house; app monitoring; MoU with Axis Energy for up to 20 GWh by 2032
Tata AutoComp–Gotion | Auto component JV (Tata group) | BESS packs and containers from 6 GWh Pune plant | - | Captive: supplies group utility Tata Power
Tesla | Global EV OEM | Powerwall 13.5 kWh (home); Megapack (utility) | - | Own energy business; #1 integrator, 46.7 GWh deployed in 2025
General Motors (GM Energy) | Global auto OEM | PowerBank 10.6 / 17.7 kWh (stack to 35.4 kWh) | Bundles from US$12,700 | Only with EV vehicle-to-home (V2H) bundles, US
BYD | EV and battery OEM | Cells and storage systems, vertically integrated | - | #1 BESS system shipper in 2025 (Benchmark)
Amara Raja | Indian battery maker | Telecom storage | – | >1 GWh telecom storage deployed
Luminous, Exide, Okaya, Loom Solar, Su-Kam | Indian inverter / battery brands | Home and small-commercial lithium storage | – | Dealer networks, sold with home inverters and rooftop solar
Ornate Solar | Indian solar company | Unity Aura C&I cabinet 100-225 kWh | – | Direct to commercial and industrial sites

## Slide 11: How a BESS charges from the grid and discharges back
1. Charging
(midday)
Solar / grid
Surplus AC power at 33 kV
Transformer
Steps voltage down to ~0.6-0.8 kV
PCS (rectifier)
Converts AC → DC
Racks + BMS
~1,280 V DC; BMS limits current and voltage
Cells store
Li⁺ moves cathode → graphite anode
2. Discharging
(evening peak)
Cells release
Li⁺ moves back to cathode; e⁻ flow out
Racks + BMS
DC out; BMS stops at low SOC
PCS (inverter)
Converts DC → AC at 50 Hz, synced to grid
Transformer
Steps voltage up to 11-33 kV
Grid / DISCOM
Power reaches homes and industry
Charging vs discharging
Item | Charging | Discharging
When | Midday, when solar is surplus and power is cheap | Evening peak after sunset
Who decides | EMS follows SLDC / DISCOM schedule | EMS follows SLDC / DISCOM schedule
Inside the cell | LiFePO₄ → FePO₄ + Li⁺ + e⁻ ; Li⁺ goes into graphite (LiC₆) | LiC₆ → 6C + Li⁺ + e⁻ ; Li⁺ returns to FePO₄
BMS stops at | Upper voltage limit (~3.65 V per cell) or full SOC | Lower voltage limit (~2.5-2.8 V per cell) or minimum SOC
Example: 1 MW / 2 MWh | Draws ~2.35 MWh over ~2-2.5 hours | Delivers 2 MWh over 2 hours at 1 MW
Losses | ~15% lost in PCS, transformer, cells and cooling (tenders require ≥85% round-trip efficiency) |